## Slide 1: Measurement Network Gateway

## Slide 2: Architecture – Block Diagram
Hardware Abstraction Layer
Sensor Interface Layer
Data Management Layer
Communication Layer
Application Layer

## Slide 3: Hardware Abstraction Layer (HAL)
The purpose of this layer is to provide a stable, versioned and unified API contract for all hardware interactions, to ensure software portability and enhanced testing.
Core functionalities:
Standardized API: All drivers (ADC, GPIO, SPI) expose functions with defined semantics like function parameters, error codes, blocking nature
Resource Lifecycle: Centralized initialization and deinitialization functions manage all system resources during system startup and shutdown.

## Slide 4: Sensor Interface Layer
Purpose of this layer is to read raw data from physical sensors with precise timing, leveraging both the FPGA (PL) and processor (PS) of zynq-7000.
Core functionalities:
FPGA (PL) for precision: Implements ADC controllers and timing critical logic in hardware for jitter free, high precision sampling.
Efficient data transfer: Uses AXI DMA to stream data directly from PL to PS memory without CPU overhead.
Interrupt Handling: GPIO buttons and critical events are handled via interrupts for immediate response.
Managing threads for each function.

## Slide 5: Data Management Layer
This layer is center for data flow, transforming raw data into calibrated, timestamped samples and managing storage. This ensures data is accurate, available for transmission.
Core functionalities:
Buffering: A thread-safe, circular buffer temporarily holds samples between acquisition and transmission
Data packaging: Applies calibration coefficients, and unit conversions to raw values. Attached high resolution timestamps.

## Slide 6: Communication Layer
Communication layer handles all network communications with the GUI client, providing a reliable, secure, and well-defined two channel protocol, so that it provides a clear separation of concerns and enables a responsive and reliable client-server interaction.
Dual channel architecture
  Data channel is a TCP server which streams live, binary-format sensor data packets to connected GUI clients.
  Command channel is a separate TCP server which is used to send configuration commands such as start/stop, set sample rate using TCF protocol.
Protocol features: Formal wire format, CRC checks, network byte order, and standard ACK/NAK responses for all commands
Connection Management: Implements heartbeats, timeouts, reconnection policies for network resilience.

## Slide 7: Application Layer
Application layer provides the end user with a comprehensive interface for real-time monitoring, historical analysis and system configuration.
Live Data Display: Shows real time sensor values and plots up to two signals on a single plot.
Control and Configuration: Sends commands to the gateway to start/stop acquisition and configure settings.
Analytics: Computes and displays simple analytics (min, max, avg, trend slope) on the client side.

## Slide 8: Threading & Reliability
To ensure the entire system operates reliably, manages concurrency safely, and can recover from faults.
Core Mechanisms:
Threading Architecture: A disciplined multi-threaded model with defined priorities and coordination using mutexes and lock-free queues to prevent priority inversion and data races.
System Lifecycle: A strict, ordered startup and graceful shutdown sequence guarantees data integrity and hardware safety.

## Slide 9: Tools
Xilinx Vivado 2022.1 for hardware packaging
Petalinux 2022.1 for embedded custom OS development
GUI client using GTK 3.0 C library