## Slide 1: Measurement Network Gateway
Haizon Helet Cruz (42708)

## Slide 2: Overview
PetaLinux basics and build process
Application Layer
  Ring buffer implementation
  Network thread implementation
GUI
  GUI Plot rendering and values text box
  Help command line

## Slide 3: Introduction
Create a Linux based software platform on Zynq
Access AXI registers implemented
Expose the hardware to C user space via character device
Enable real-time sensor data acquisition
Software Stack
User-Space App (mngivp.c)
Character Device /dev/meascdd
meascdd.ko Kernel Module
Linux Kernel + Device Tree
AXI IP Core (PL – Vivado)
Physical Sensors (ADC, Temp, GPIO)

## Slide 4: Image Build Process
STEP 1 – Create Project
petalinux-create
--type project
--template zynq
--name meas_gateway
Yocto-based Linux build environment for ARM Cortex-A9
STEP 2 – Import XSA
petalinux-config
--get-hw-description
=<file_path>
Auto-generates DTS, DTSI, kernel config fragments
STEP 3 – Verify DTS
system-top.dts
pl.dtsi
Kernel config frags
AXI base address & interrupt ID must match Vivado
STEP 4 – Build
petalinux-build
Generates full Linux image aligned with Zynq-7000 hardware

## Slide 5: Image Build Process - Hardware and Device tree
We have a custom FPGA board with any number of sensors, the question is how do we make it accessible.
In FPGA, we have custom IP core "measdif"
Device tree entry has "compatible", "reg", "interrupt". Auto generated from .xsa
Shared header - Communication contract between kernel and user space
typedef struct {
unsigned int rnum; // which register
unsigned int rvalue; // its value
} MeasObj_struct;

## Slide 6: Image Build Process - Kernel
Once the "compatible" string is matched, the probe function is called.
This is accessible using methods dev_open, dev_write, dev_read, dev_release

## Slide 7: Image Build Process - Read and Write
Read process
write({rnum = 0xFF, rvalue = N}), selects register N
read(), get register N‘s value
Write process
write({rNum = N, rValue = value}), write value to register N
petalinux-build : compiles kernel + driver + rootfs + u-boot
petalinux-package --boot : Creates BOOT.BIN + image.ub + rootfs.ext4
Flash to SD card and boot the board

## Slide 8: Application - Network Layer
Haizon Helet Cruz (42708)

## Slide 9: Application Layer Overview
01
Ring Buffer — Fundamentals
Fixed-memory FIFO, producer–consumer model, O(1) complexity
02
Ring Buffer — Concurrency
Mutex protection, condition variables, overflow policy
03
Ring Buffer — Operations
Insert (O1), batch extraction, complexity analysis
04
TCP Network Thread
Socket creation, Berkeley Sockets API, server lifecycle
05
State Machine
IDLE → RUNNING → DISCONNECT states and transitions
06
Configuration Commands
CONNECT, START, CONFIGURE, STOP, DISCONNECT, SHUTDOWN

## Slide 10: Ring Buffer Role in MNG
Ring Buffer is a common data storage method used in embedded systems.
This data structure enables in active communication between the two threads
  Sensor thread can "fire and forget"
  Network thread focuses on retrieving data and send to the GUI

## Slide 11: Ring Buffer Operations
Ring Buffer Init - ring_buffer_t *ringBufferInit()
Ring Buffer add sample - void ringBufferAddSample(ring_buffer_t *rb, const sensor_data_t *sample)
Ring Buffer batched data extraction - size_t ringBufferRemoveBatch(ring_buffer_t *rb, sensor_data_t *dest, size_t max_samples)
Free memory allocation - free(rb)
Ring Buffer structure
typedef struct {
pthread_mutex_t rbMutex;
sensor_data_t sampleArray[RING_BUF_SIZE];
size_t write_index;
size_t read_index;
uint16_t count;
} ring_buffer_t;

## Slide 12: TCP Network Thread - Configuration Commands
CONNECT <ip_address> : Connect to device using IPv4 address
START : Start to send data to the GUI. IDLE to RUNNING state
CONFIGURE : configure <sensor_identifier> <sampling_frequency>
STOP : Stop sending data to the client. RUNNING to IDLE state
DISCONNECT : Disconnects from client. IDLE to DISCONNECT state
SHUTDOWN : Shuts down the server

## Slide 13: TCP Network Thread - Workflow

## Slide 14: GUI Render Flow Pipeline

## Slide 15: Tasks Completed
Theoretical study on PetaLinux implementation
Ring Buffer Implementation
Network Thread Implementation
GUI rendering, value text box and help command line
Adding suggested improvements and debugging bugs